## Slide 1
STRUCTURAL INSPECTION · COMPUTER VISION
Computer Vision Based Structural Concrete Crack Measurement Gauge (CRACKGAUGE)
From Manual Inspection to Digital Crack Measurement
Raspberry Pi
Computer Vision
OpenCV
Image Processing
Digital Reporting
TEAM MEMBERS
Manish Saini
Ayush Gigras
Sachin Chauhan
Mentor: Anuska Shukla
Concrete Wall
Camera Device
Crack Detection
Width · Length · Orientation
Digital Report
01 / 12
Notes: Our project aims to develop a low-cost portable system that can capture concrete cracks using a camera and automatically detect and measure their width, length and orientation. Instead of relying completely on manual visual measurement, our system combines controlled imaging, computer vision and physical calibration to produce digital inspection records.

## Slide 2
THE CHALLENGE
The Problem With Manual Crack Inspection
Concrete cracks develop due to
•
Structural loading
•
Shrinkage & thermal effects
•
Environmental exposure
•
Aging and deterioration
Current inspection process
Visual Inspection
Manual Crack Measurement
Manual Recording
Report Preparation
Key Problems
1
Time-consuming
Inspectors must manually locate and measure every crack.
2
Subjective
Results vary by person, viewing angle and measurement method.
3
Poor digital traceability
Measurements, images and locations are recorded separately.
4
Hard to track progress
Comparing the same crack across inspections is inconvenient.
WHY THIS MATTERS
>3mm
crack width is a recognised trigger for a formal structural audit
30–50 yrs
building age when Indian municipal bodies mandate periodic audits
₹60K–1.2L
typical professional structural audit cost, mid-rise building
The real challenge isn't detecting a crack - it's measuring it consistently and keeping a digital history of how it changes over time.
02 / 12
Notes: The problem is not simply detecting whether a crack exists. The real challenge is measuring it consistently and maintaining a digital history of how it changes over time. Cracks wider than about 3mm, or buildings past the age thresholds cities set for mandatory audits, are exactly where consistent measurement matters most - yet today it still depends on a person with a tape and a notebook.

## Slide 3
LANDSCAPE
How Is It Done Today?
Method
Advantage
Limitation
Crack Comparator Card
Cheap & simple
Manual reading
Handheld Microscope
More precise
Requires trained operator
Digital Crack Gauge
Digital measurement
Costly
Smartphone Apps
Portable
Accuracy depends on imaging/calibration
ACI identifies crack comparators and scaled optical devices such as handheld microscopes as established crack-width measurement approaches.
The Gap
Low cost →
Automation →
Manual
Comparator
Digital Gauge
Our Target
Low-cost + Portable + Calibrated + Automated + Digitally Traceable
Existing manual tools are affordable but need human measurement; digital gauges automate but cost more; smartphone apps are portable but accuracy hinges on imaging and calibration. Our target is the middle ground.
A 2025 study on smartphone-based concrete crack-width measurement stresses standardized calibration and repeatable testing as the key validation requirement.
03 / 12
Notes: Existing manual tools are affordable but require human measurement. Commercial digital gauges provide automation but can be expensive. Smartphone-based approaches provide portability, but engineering accuracy depends strongly on imaging and calibration. Our project targets the middle ground: a low-cost physical device with controlled imaging and computer-vision-based measurement.

## Slide 4
OUR ANSWER
Our Solution: CrackGauge
①
Captures
Concrete surface image under controlled lighting.
②
Detects
Automatically extracts crack regions.
③
Measures
Calculates max width, avg width, length, orientation.
④
Calibrates
Converts pixels to millimeters via a physical marker.
⑤
Records
Stores image + measurements + timestamp.
⑥
Reports
Generates a digital inspection report.
CRACKGAUGE
Hardware
• Camera
• LED
• Marker
Vision Engine
• OpenCV
• Mask
• Measure
Digital Platform
• Dashboard
• Database
• PDF
Not just a crack-detection app - a complete inspection system: physical imaging device + vision measurement engine + digital reporting platform.
04 / 12
Notes: Our solution is not just a crack detection app. It is a complete inspection system consisting of a physical imaging device, a computer vision measurement engine and a digital reporting platform.

## Slide 5
HARDWARE
Portable Crack Measurement Gauge
CONCRETE SURFACE
crack
REFERENCE MARKER
fixed distance
LED RING
+ CAMERA
Raspberry Pi
Components
Raspberry Pi 4 (4GB)
Pi Camera / USB Camera
LED Ring Light
ArUco / Reference Marker
Fixed-distance Spacer
3D-Printed Enclosure
Power Bank
Optional USB Microscope
APPROXIMATE PROTOTYPE COST
₹9,000 – ₹14,000
Design decision
We don't just point a camera at the wall - imaging is controlled. The LED gives consistent illumination, the spacer keeps camera distance fixed, and the marker gives physical scale for calibration.
05 / 12
Notes: The important design decision is that we are not simply pointing a camera at the wall. We want to control the imaging conditions. The LED provides consistent illumination, the spacer maintains approximately fixed camera distance, and the reference marker provides physical scale for calibration.

## Slide 6
FULL STACK
Complete System Architecture
Camera + LED
Raspberry Pi - Image Capture
Image Quality Check
Calibration & Perspective Correction
Preprocessing
Hessian / Ridge Filtering
Adaptive Thresholding
Crack Mask
Width
Length
Orientation
Calibrated to mm → stored in database & PDF dashboard
Three layers
1
Hardware
Captures a controlled image of the concrete surface.
2
Vision Processing
Segments the crack and extracts its geometric properties.
3
Digital Reporting
Calibration converts pixels to millimeters; results are stored and displayed.
Don't read every box - walk the audience through hardware → vision → reporting.
06 / 12
Notes: Our architecture has three major layers: hardware, vision processing and digital reporting. The camera captures a controlled image. The vision engine segments the crack and extracts its geometric properties. Finally, calibration converts pixel measurements into physical millimeter values, which are stored and displayed digitally.

## Slide 7
VISION PIPELINE
How Will The Crack Be Detected?
Input Image
Grayscale
Noise Reduction
Contrast Enhancement
Hessian / Ridge Filtering
Adaptive Thresholding
Morphological Processing
Crack Segmentation
Why these techniques?
Hessian / Ridge Filtering
Emphasizes thin, elongated crack-like structures.
Adaptive Thresholding
Handles uneven illumination better than one global threshold.
Morphological Processing
Removes noise and cleans up the crack mask.
Output
ORIGINAL IMAGE
CRACK MASK
07 / 12
Notes: Concrete surfaces are not clean backgrounds. They contain texture, stains, shadows and irregularities. Therefore, a simple threshold is not sufficient. Our proposed pipeline uses Hessian-based ridge enhancement to highlight line-like crack structures, followed by adaptive thresholding and morphology to obtain a cleaner crack mask.

## Slide 8
FROM PIXELS TO GEOMETRY
How Will We Measure The Crack?
From crack mask → physical measurement
Width
Crack Mask
Skeletonization
Distance Transform
Local Width
If distance from skeleton to boundary = D pixels
Width ≈ 2D pixels
Length
Crack Skeleton
Path Length
Pixel Length
mm Length
Skeleton path length, scaled from pixels to millimeters.
Orientation
Crack Coordinates
PCA
Dominant Direction
Angle in Degrees
Principal Component Analysis finds the crack's dominant direction.
After segmentation, the skeleton gives the crack's centerline; distance-transform gives local width; the skeleton path gives length; PCA gives dominant orientation.
08 / 12
Notes: After segmentation, we convert the crack into a skeleton representing its centerline. Distance transform gives us the local distance from the centerline to the boundary, allowing us to estimate crack width. The skeleton path gives crack length, while PCA gives the dominant crack orientation.

## Slide 9
CALIBRATION
How Do Pixels Become Millimeters?
The camera sees pixels. The engineer needs millimeters. So, we use a known physical reference.
EXAMPLE
Reference marker = 50 mm
Detected marker = 400 pixels
Scale = 400 / 50 = 8 pixels/mm
If crack width = 12 pixels:
Crack Width = 12 / 8 = 1.5 mm
Calibration matters because a pixel has no fixed physical size across imaging conditions - the reference marker and controlled camera geometry fix the pixel-to-mm scale before we calculate crack dimensions.
CRACKGAUGE REPORT
Maximum Width
1.50 mm
Average Width
0.82 mm
Length
84.3 mm
Orientation
47°
Severity
Moderate*
Date
04/09/26
Original Image
Crack Mask
*Severity thresholds are configurable and will be validated against engineering references; the prototype alone does not determine structural safety.
09 / 12
Notes: Calibration is critical because a pixel does not have a fixed physical size in every imaging condition. By using a known reference marker and controlling camera geometry, we estimate the pixel-to-millimeter scale before calculating the crack dimensions.

## Slide 10
MARKET LANDSCAPE
Where Does Our Solution Stand?
Feature
Manual Gauge
Digital Gauge
Smartphone App
CrackGauge
Crack Detection
✕
!
✓
✓
Width Measurement
✓
✓
✓
✓
Length Measurement
✕
!
✓
✓
Orientation
✕
!
!
✓
Digital Image
✕
✓
✓
✓
Controlled Lighting
✕
!
✕
✓
Inspection History
✕
!
!
✓
Commercial digital gauges (e.g. SISCO) already offer image/data storage over a stated 0–10 mm width range; smartphone apps (e.g. Crack Detector) already use marker-based mm calibration for width and length. We're not claiming crack measurement is new.
Our differentiation:
Controlled physical imaging + computer-vision measurement + digital inspection history, combined in one low-cost device.
10 / 12
Notes: We are not claiming that crack measurement itself is new. Existing manual gauges, digital instruments and smartphone applications already address parts of the problem. Our differentiation is the combination of controlled imaging, physical calibration, automated multi-parameter measurement and digital traceability in a low-cost prototype.

## Slide 11
PROOF
Ground-Level Research & Validation
1
Ground-Level Research
Interview civil engineering faculty, site engineers, structural inspectors, contractors.
Q1. How are cracks measured today?
Q2. What tools are used?
Q3. Biggest difficulty?
Q4. Would digital records help?
2
Controlled Testing
Concrete specimens with different:
• Crack widths
• Crack orientations
• Surface textures
• Lighting conditions
• Camera distances
3
Compare vs Ground Truth
Ground Truth / Manual Reference
COMPARE
CrackGauge Measurement
Validation Metrics
Measurement
MAE
RMSE
Relative Error
Detection / Segmentation
Precision
Recall
F1
IoU / Dice
System
Repeatability
Processing Time
We don't want to show the system only produces a number - we need to show that number is close to a reliable reference, across widths and imaging conditions.
11 / 12
Notes: We don't want to demonstrate only that the system produces a number. We need to demonstrate that the number is close to a reliable reference measurement. Therefore, we will test different crack widths and imaging conditions and calculate measurement error and repeatability.

## Slide 12
THE ROAD AHEAD
Roadmap & Expected Impact
P1
Camera + Sample Images
P2
Crack Segmentation
P3
Width/Length/Orientation
P4
Physical Calibration
P5
RPi Prototype
P6
Dashboard + Database
P7
Validation
FINAL PROTOTYPE
Expected Final System
Portable
Easy to carry during inspection
Low-cost
Uses affordable hardware
Automated
Reduces manual measurement effort
Calibrated
Converts image measurements to physical units
Digital
Images + measurements + timestamps
Trackable
Future inspections can be compared
Future: Crack Growth Analysis
Insp. 1 – 0.40mm
Insp. 2 – 0.52mm
Insp. 3 – 0.71mm
Our goal is to move concrete crack inspection from manual observation to measurable, repeatable and digitally traceable inspection.
Thank You
12 / 12
Notes: Our goal is to move concrete crack inspection from manual observation to measurable, repeatable and digitally traceable inspection. Thank you.

## Slide 13
Notes: Our goal is to move concrete crack inspection from manual observation to measurable, repeatable and digitally traceable inspection. Thank you.